!
! 	Beam Trimming 
!
! We can now edit Sea Beam data beam by beam for contouring & gridding.
!
! Beam trimming is done much like time windowing; in fact it
! is simply an extension of time windowing.  An optional addition
! to either an INCLUDE or an EXCLUDE window controls beam trimming.
! No changes are required to current time windows; they will work as
! they always have.
! 
! Beams are numbered as follows:
! 
!     port                                                 stbd
!      P9 P8 P7 P6 P5 P4 P3 P2 P1 0 S1 S2 S3 S4 S5 S6 S7 S8 S9
! 
! The center beam is number 0.
! 
! You choose a portion of a ping by selecting from one beam
! to another beam, for instance P9 to P3 or P3 to S3.  The selected 
! area can either be included or excluded. 
! If for any reason you need to window more than one continuous group of
! beams within any given area (e.g., you want to exclude P9 to P3 and S2 to S4)
! you must use two windows, one for each group.
!
! Some examples should make the convention clear.
!

!______________________________________________________________________
!
! 	Sample Window file 
!
! the following two lines include ALL available beams between the
!  listed times.
!
INCLUDE 29-SEP-1984 14:10:00 TO 29-SEP-1984 16:10:00 
INCLUDE 29-SEP-1984 16:50:00 TO 29-SEP-1984 19:10:00
!
! this line excludes ALL beams in this time window.
!
EXCLUDE 29-SEP-1984 17:50:00 TO 29-SEP-1984 18:00:00 
!
!
!                                                 
!       These windows include or exclude specific beams
!                                                                  
! This line gets rid of some beam curl found on port & stbd outer beams
!
INCLUDE 29-SEP-1984 16:20:00 TO 29-SEP-1984 16:50:00 BEAMS P6 TO S6
!
! This line includes the center 9 beams for the data within this time
!
INCLUDE 29-SEP-1984 16:50:00 TO 29-SEP-1984 19:10:00 BEAMS P4 TO S4
!
! exclude a brief section of 3.5 kHz interference on the port side.             
!
EXCLUDE 29-SEP-1984 18:00:00 TO 29-SEP-1984 18:05:00 BEAMS P4 TO P9
!
! include only the beam to port of the center beam for this section
!
INCLUDE 29-SEP-1984 18:05:00 TO 29-SEP-1984 18:10:00 BEAM P1
!
! include only the center beam for this section
!
INCLUDE 29-SEP-1984 18:10:00 TO 29-SEP-1984 18:15:00 BEAM 0 
!
!  use only the center & port beams because of swath overlap and
!                     redundant data
!
INCLUDE 29-SEP-1984 18:15:00 TO 29-SEP-1984 18:55:00 BEAM 0 TO P9
! 
!______________________________________________________________________
!
! What is actually occurring is that each time window now has a
! "swath window" associated with it.  That swath window is a 
! bit map of the swath.  Each ping that falls within a time window
! gets compared to the corresponding bit map and the rejected beams 
! get zeroed out before plotting.                            
!
! You will be able to view swaths with each ping marked using an
! upgraded contour program.  The last question in a contour
! input file will ask if you want each beam annotated or not.  The
! default answer is NO.  If you respond YES, each beam point containing
! data has a symbol centered over it.  Port beams are marked with a 
! tiny triangle, starboard beams with a diamond and the center beam with
! a slightly larger octagon.  This takes quite a while to plot but is very
! helpful in doing precise beam trimming to weed out bad pings and unwanted 
! data.  Careful beam trimming will remove many artifacts in a gridded map.
!
! The convention for plotting a track line using a window file
! that contains beam trimming is that if ANY beams are to be plotted
! a track line is drawn.
!